| Form 8.1 Troubleshooting guide |
| --- |
|  |  |  |  |  |  |  |  |  |  |  |  |  | Page 1/3 |
| Survey completed by: _________________________ | Reference #: ________________________________ |
| Client contact information |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | Yes | No |
| Client name: ___________________________________ | Time: ______________ | Date: _______________ |
| Address: ____________________________________________________________________________________ |
| Phone #: ___________________________________ | Cell #: __________________________________ |
| Designer: _______________________________________ | Installer: __________________________________ |
| Design flow: _________________________________GPD | Date of last pumpout: _______________________ |
| Is the facility in a rural setting? |  |  | ( | ( |
| Basics of troubleshooting |
| 1. | Research claims |  |  |
|  | a. | Technology is able to handle : |  |  |
|  | Hydraulic loading: | ____ gpd | Organic loading: | ____ mg/L | Mass loading: | ______ lbs/day |
|  | b. | List possible interferences: ___________________________________________________________ |
| 2. | Review plans |  |  |
|  | a. | Hydraulic loading (design): | Peak flow: _______ gpd | Average flow: _________ gpd |
|  |  | Hydraulic loading (actual): | Peak flow: _______ gpd | Average flow: _________ gpd |
|  | b. | Organic loading: ________________ lbs/day (BOD5) | Actual: ___________________ lbs/day |
|  | c. | Number of people living in the house: |  |  |  |  |
|  |  | i. | Design |  |  |
|  |  | Adults: | Teenagers: | Children: |
|  |  | M | ___ | F | ___ | M | ___ | F | ___ |  | M | ___ | F | ___ |  |
|  |  | ii. | Actual |  |  |
|  |  | Adults: | Teenagers: | Children: |
|  |  | M | ___ | F | ___ | M | ___ | F | ___ |  | M | ___ | F | ___ |  |
|  | d. | Number of bedrooms: ____________ (design) | Number of bedrooms: ____________ (actual) |
|  | e. | Number of bathrooms: ___________ (design) | Number of bathrooms: ___________ (actual) |
|  | f. | Days of operation | Plan: ____________ | Actual: _____________ |
| 3. | Review regulations |  |  |  |  |  |  |  |  |  |
|  | a. | Is system compliant with regulations? |  |  |  |  |  |  |  | ( | ( |
|  | b. | Are regulations the cause of malfunction? |  |  |  |  |  |  |  | ( | ( |
| 4. | Determine the source |
|  | a. | Has evaluation survey been filled out by system owner or manager? | ( | ( |
| 5. | Constituent testing |  |  |
|  | a. | Has the system been sampled? |  |  | ( | ( |
|  | b. | Please list any constituents that are out of the expected range: _______________________________ |
| 6. | Operation and maintenance |  |  |
|  | a. | Has proper O&M been performed on the system according to the plans? | ( | ( |
| 7. | System accessibility |
|  | a. | Is wastewater treatment system accessible at the surface? |  | ( | ( |
| 8. | Power outages |  |  |  |
|  | a. | Have there been recent power outages in the system? |  | ( | ( |
| 9. | System misuse |  |  |  |
|  | a. | Is the facility owner aware of the dos and don’ts of onsite wastewater treatment systems? | ( | ( |
|  | b. | Has the system been used properly? |  | ( | ( |
| 10. | Clear water addition |  |  |  |
|  | a. | Is clear water being added to the onsite wastewater treatment system? |  | ( | ( |

|  |  |  |  |  |  |  |  |  |  |  |  |  |  | Page 2/3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | Yes | No |
| System history |  |  |  |  |  |  |  |  |  |
| 11. | How old is the system? ___________________ years |
| 12. | Has the system ever backed up? | ( | ( |
| 13. | Are baffles present Have the baffles ever plugged? |  | ( ( | ( ( |
| 14. | Has the system ever been repaired? | ( | ( |
| 15. | Has effluent ever surfaced? | ( | ( |
| 16. | Has the alarm ever sounded? | ( | ( |
| Site evaluation |  |  |
| 17. | Percolation or infiltration test: |  | __________ gal/foot2/day |
| 18. | Groundwater table |  |  |  |  |  |  |  |  |
|  | a. | Seasonal : ________ in. |  |  |  |  |  |  |  |  |
|  | b. | Average: _________ in. |  |  |  |  |  |  |  |  |
| 19. | Property use |  |  |  |  |  |  |  |  |
|  | a. | Is the system free of encroachments? |  | ( | ( |
|  | Driveways: ( | Patios: ( | Utility easements: ( | Decks: ( | Livestock: ( |
|  | Gardening: ( | Pets: ( | Vehicular traffic: ( | Construction: ( | Other: ( _________ |
| 20. | Topography and landscape position |  |
|  | a. | Is surface water effectively managed/diverted away from site? | ( | ( |
|  | b. | Is surface water effectively managed/diverted away from system and components? | ( | ( |
|  | c. | Are the system components free from settling or erosion? | ( | ( |
| 21. | Subsurface water management |  |
|  | a. | Type: | Gravity: ( | Pump: ( | Not present: ( |
|  | b. | Outlet open to drainage |  |  | ( | ( |
|  | c. | Rodent guard on outlet |  |  | ( | ( |
|  | d. | Is the sump pump working? |  |  | ( | ( |
|  | e. | Outlet for sump pump discharge |  |  | ( | ( |
| 22. | Vegetation |  |  |  |  |
|  | a. | Trees in distribution field |  |  | ( | ( |
|  |  | i. | Type(s): ______________________________________________________________________ |
|  |  | ii. | Location(s): ___________________________________________________________________ |
|  | b. | Excessive vegetation |  |  | ( | ( |
|  |  | i. | Location(s): ___________________________________________________________________ |
|  | c. | Uneven vegetation |  |  | ( | ( |
|  |  | i. | Location(s): ___________________________________________________________________ |
|  | d. | Poor vegetation | ( | ( |
|  |  | i. | Location(s): ___________________________________________________________________ |
| Storage and pretreatment components |  |  |  |  |  |  |  |
| 23. | Septic tank size: ___________ gal | HDT: _________________ days |
| 24. | Sludge levels in septic tank: |  |
|  | Sludge: ________ inches | Clear: ________ inches | Scum: ________ inches |
| 25. | a. | Effluent screen in septic tank outlet |  |  | ( | ( |
|  | b. | Has effluent screen ever been plugged? |  |  | ( | ( |
| 26. | Grease trap |  |  | ( | ( |
|  | a. | Is it in acceptable condition? | ( | ( |
| 27. | Flow equalization tank | ( | ( |
|  | a. | Is it in acceptable condition? | ( | ( |
| 28. | Holding tank | ( | ( |
|  | a. | Is it in acceptable condition? | ( | ( |
|  |  |  | Page 3/3 |
|  |  |  | Yes | No |
| Advanced pretreatment components |  |  |
| 29. | Indicate the presence of the following components: |  |  |  |
|  |  | Media filter: ( | ATU: ( | Disinfection unit: ( |
| Type:____________________ _________________ _____________________ |
| Final treatment and dispersal system |  |  |
| 30. | Soil type at soil treatment area depth or lower: __________________________________________________ |
| 31. | Type of distribution/dispersal system: _________________________________________________________ |
| System controls |  |
| 32. | Dosing tank size: ___________________ gal. |  |  |  |  |  |  |
| 33. | Sludge level in dosing tank: _______________________ inches |  |  |  |
| 34. | Correct setting of time components |  |  |  |  |  | ( | ( |
|  | ON: | ______ | OFF: | ______ | Man: ( | Auto: ( | Off: ( |  |  |  |  |
| 35. | Is the pump working? | ( | ( |
| 36. | Duration of pump cycle |  |  |
|  | Pump run time: __________ | Present meter reading: ____ | Last meter reading: ______ |  |  |
| 37. | Pump drawdown |  |  |
|  | GPI: ____ | Drawdown: ________ inches | Pump delivery rate: ___________gpm |  |  |
| Microscopic Examination:_______________________________________________________________________ ____________________________________________________________________________________________________________________________________________________________________________________________ Additional Comments____________________________________________________________________________ __________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________ |

Site Sketch