Form 8-5 Operational Checklist: Dripfield (DF)

Service provided on:   Date:               	Time:                        		Reference #:

Service provided by:   Company: 				     	  	Employee:

Date of last service: 		 		By:  ( You   ( Other:

Date of last inspection: _______________________________

1.	Conditions at the drip distribution zone

a.	Evaluate presence of odor within 10 ft of perimeter of system:

( None     ( Mild     ( Strong     ( Chemical    ( Sour

b.	Source of odor, if present: _________________________________

c.	Indications of leaks around/above system.	Yes	No

d.	Vegetation appropriate.	Yes	No

e.	Excessive vegetative growth.	Yes	No

f.	Vegetation adequately maintained.	Yes	No

g.	Preventing accessibility for maintenance.	Yes	No

2.	Drip filter

a.	Type of filter:

( Sand	( Screen	( Disk	( Other:

b.	Filter in place.	Yes	No

c.	Pre-filter pressure:			 PSI

d.	Post-filter pressure:			 PSI

e.	Filter:	( Cleaned	( Replaced

f.	Automatic cleaning operational.	N.A.	Yes	No

g.	By-pass flow operating.		N.A.___	Yes	No

h.	Boxes insulated.	N.A. ___Yes	No

i.	Heater pad operational.	N.A. ___Yes	No

3.	Effluent flow metering

a. 	Flow meter:

Current (PFR):	 _____gal     Date: _________

Previous (LFR):_____gal     Date:	________

Differential ( [PFR – LFR] / days):

_____gpd    Days:	________

4.	Switching valves

a.	Switching valve present.	Yes	No

b.	Type of valve:

c.	Operating properly.	Yes	No

d.	Action taken if not:

5.	Field flushing: 	( None	( Manual	( Automatic	( Continuous

a.	Operational.						Yes	No

| Zone | Manually Flushed Zones | Operating Pressure (PSI) | Zone Flushing | Field Dosing |
| --- | --- | --- | --- | --- |
|  |  | Dosing | Flushing | ETM | CC | ETM | CC |
|  |  |  |  | PFTR | LFTR | PFCR | LFCR | PFTR | LFTR | PFCR | LFCR |

b.	Field flushing operation:

Reference #:

6.	Zone operation:

| Zone | Flow Rate (gpm) | Total Flow (gal) (since last visit) | Air/Vacuum relief operating | Surfacing Effluent |
| --- | --- | --- | --- | --- |

7.   Manufacturer’s required maintenance performed.	Yes	No

(If ‘Yes’, attach Manufacturer Inspection form to this report, if supplied)

CC- cycle counter

ETM- elapsed time meter

GPM- gallons per minute

LFCR- last flushing cycle reading

LFR- last flow meter reading

LFTR- last flushing time reading

PFCR- present flushing cycle reading

PFR- present flow meter reading

PFTR- present flushing time reading

PSI- pounds per square inch

TT- total time

# Text boxes

NOTES

1.  ( Acceptable

( Unacceptable

2.  ( Acceptable

( Unacceptable

3.  ( Acceptable

( Unacceptable

4.  ( Acceptable

( Unacceptable